## Slide 1
SMART INDIA HACKATHON 2026 · IDEA SUBMISSION
SIH logo
Intelligent RF
Spectrum Scan Strategy
A wideband receiver can listen to only 2 of 16 bands at a time. We learn which 2 — and when.
PROBLEM STATEMENT ID
[ fill in from the portal ]
THEME
[ fill in from the portal ]
PROBLEM STATEMENT TITLE
Intelligent RF Spectrum Scan Strategy
PS CATEGORY
Software
TEAM ID
[ fill in from the portal ]
TEAM NAME
[ your registered team name ]
Heard — receiver tuned here, emitter active
Tuned, but the band was quiet
Active, and missed — nobody was listening
16 bands across · time flowing down · K = 2 tuned at any instant
Simulation-only. No RF hardware, no interception, no jamming, no weapon control.
1
Notes: Open on the picture, not the title. Sixteen bands across, time flowing down. Blue cells are emitters transmitting. Amber is where our receiver actually was. Every blue cell is signal we lost forever, because a receiver hears two bands at a time and there are sixteen. That gap is the whole problem statement. Everything after this slide is about closing it.

## Slide 2
PROPOSED SOLUTION
SHRUTI — learning where to listen, and when
Today the receiver sweeps bands in a fixed order. Four out of five dwells land on empty air, and short bursts are lost between visits. SHRUTI replaces the sweep with a policy that decides, every step, which bands are worth hearing next.
HOW THE SOLUTION WORKS
1
Model the spectrum
16 bands, 10 emitters across five behaviour classes — fixed, periodic, agile, random, intermittent. Deterministic by seed.
2
Predict the rhythm
Ai-ml-2 folds each band's detection times onto candidate periods and returns a next-activation window with a calibrated confidence.
3
Decide where to listen
Ai-ml-1 reads per-band state — time since scan, detection EWMA, misses, periodicity phase — and picks the next K bands.
4
Learn from the outcome
Each step returns a reward and updates the policy online. Scoring uses ground truth the scheduler is never shown.
INNOVATION AND UNIQUENESS
We observe our detections, not the emitter.
The median gap between detections measures the scan schedule, not the signal. Phase folding recovers the true period even when whole cycles went unheard.
Confidence that survives the search.
p-values are corrected for the number of independent trial periods, so the four non-periodic emitter classes sit at the nominal 5%, not 99%.
The trade-off is a dial, not an accident.
One reward weight moves the policy monotonically between hearing more spectrum and catching more distinct bursts. Retuned per mission.
Measured on Scenario B — 16 bands, 10 emitters, 5 seeds, 1000 steps, every policy on an identical spectrum.
2
Notes: One sentence for the whole idea: the receiver stops sweeping and starts choosing. The second innovation is the one to dwell on if a signals person is judging. We never see the emitter. We only see our own detections of it, and those gaps are set by our scan schedule, not by the transmitter. Taking the median of them measures ourselves. Phase folding is what gets past that.

## Slide 3
TECHNICAL APPROACH
Four services, one contract, a decision every 6.6 ms
SYSTEM ARCHITECTURE
Frontend
React 18 · TS · Vite
Backend
Spring Boot 3
system of record
PostgreSQL · Redis
Ai-ml-1
scan policy
:8500
Ai-ml-2
periodicity
:8600
The Frontend talks only to the Backend. The Backend is the only caller of either ML service, and assembles the state vector before it asks for a decision.
API_CONTRACT.md is copied byte-identical into all four folders — one source of truth, four independently buildable teams.
PER-STEP DECISION LOOP
01
Advance the spectrum one step
02
Ai-ml-2 predicts each band's next window
03
Backend builds the state vector
04
Ai-ml-1 returns the next K bands
05
Scan, detect, score against ground truth
06
Reward goes back — the policy updates
6.6 ms p95 decide over HTTP, 50 ms budget
3.0 ms p95 periodicity, 64 bands
TECHNOLOGY STACK
Backend
Java 21
Spring Boot 3
PostgreSQL
Flyway
Redis
WebSocket
Machine learning
Python 3.12
FastAPI
Gymnasium
NumPy / SciPy
Stable-Baselines3
Frontend and ops
React 18
TypeScript
Vite
Docker
Prometheus
pytest / JUnit
3
Notes: The seam to point at is the contract. Four folders, one API_CONTRACT.md copied into each, so the two ML services, the backend and the frontend were built in parallel without blocking each other. If asked about latency, be precise: 6.6 ms is p95 over a real HTTP socket, not an in-process call. The in-process number is about forty times faster and it would be dishonest to quote it, because the backend pays the socket.

## Slide 4
FEASIBILITY AND VIABILITY
It runs today, and we know where it loses
WHAT ALREADY RUNS
Four services, one command each, Dockerised, booting on H2 or Postgres with no other setup.
Deterministic by seed — the same seed gives every policy an identical spectrum, so comparisons are like for like.
A one-button scripted demo: live waterfall, running metrics, then the baseline-versus-learned comparison.
DQN and PPO are built and verified behind a flag; the bandit is the default because it needs no pre-training.
167
tests, scheduler
77
tests, estimator
96%
coverage, Ai-ml-2
87%
coverage, Ai-ml-1
Simulation-only by design. The policy consumes an abstract per-band state vector, so no code path touches a radio.
CHALLENGES, AND HOW WE HANDLE THEM
The learned policy does not win everything.
It catches fewer distinct bursts than the sweep — 0.174 against 0.413.
A real resource frontier, not a defect. With K = 2 of 16 you either spread thin and clip the start of many bursts, or concentrate and hear far more air. One reward weight moves along it monotonically, and is retuned per mission.
Raw intercept time ranks the better policy worse.
It averages only the bursts a policy actually caught.
We report censored intercept time beside it, charging every undetected burst the full episode, so the average is defined over all bursts rather than the easy ones.
The periodicity service cannot help end to end yet.
It is told when a detection happened, never when a band was heard and found silent.
Diagnosed, with a named fix: carry scanned-but-empty observations in the contract. The acceptance test stays in the suite, disabled with this reason, so the gap cannot quietly go stale.
4
Notes: This is the slide that wins or loses the room. Every other team claims their model beats the baseline on everything. Say the weakness out loud before a judge finds it: we lose distinct-burst coverage to the sweep, and here is the reward weight that trades one for the other. The third risk is an open item. Do not hide it. It is understood, the fix is named, and the failing test is still in the suite rather than deleted. A judge who finds an honest team stops looking for exaggeration everywhere else.

## Slide 5
IMPACT AND BENEFITS
Three times the detection rate, from the same receiver
3.2×
Detection rate
Pd 0.107 → 0.345
3.7×
High-priority detection
HPDR 0.101 → 0.375
2.9×
Listening efficiency
0.198 → 0.573 of dwell on live air
6.6 ms
Decision latency
p95 over HTTP, 50 ms budget
ROUND-ROBIN SWEEP VERSUS THE LEARNED POLICY
Chart: 
| Detection rate | High-priority | Listening efficiency
Round-robin sweep | 10.7 | 10.1 | 19.8
SHRUTI (learned) | 34.5 | 37.5 | 57.3
WHO IT SERVES
Operational
Spectrum-monitoring and EW operators hear more of the band plan from the receiver they already own — a capability gain in software, with no extra RF front-ends.
Economic
A reproducible testbed lets scan strategies be compared, and rejected, before any hardware is committed to a programme.
Scientific
The phase-folding estimator and the censored-average metric generalise to any sparse, irregularly sampled event series.
Scenario B · 16 bands · 10 emitters · 5 seeds · 1000 steps · every policy on an identical spectrum per seed
5
Notes: Lead with the chart, not the tiles. Same spectrum, same seeds, same receiver, only the scheduler changed. Listening efficiency is the number an operator feels: the fraction of dwell time spent on air that actually had something in it. It goes from one fifth to well over half. If asked what this costs to deploy, the answer is a software change on an existing receiver, which is the whole economic argument.

## Slide 6
RESEARCH AND REFERENCES
Measured against the baselines it replaces
SCENARIO B RESULTS — 5 SEEDS, 1000 STEPS
Metric | Random | Round-robin | SHRUTI
Detection rate (Pd) | 0.104 | 0.107 | 0.345
High-priority detection | 0.109 | 0.101 | 0.375
Listening efficiency | 0.190 | 0.198 | 0.573
False-alarm rate (Pfa) | 0.069 | 0.068 | 0.070
Distinct bursts caught | 0.340 | 0.413 | 0.174
Green marks where the sweep still wins. We report it rather than dropping the row.
Prototype and source
Repository: [ add your GitHub link ] Demo video: [ add your link ]
scripts/compare.py reproduces every number on this slide from a clean checkout.
PRIOR ART
US 10,523,342 B1 — Autonomous RL method of receiver scan schedule control. BAE Systems.
Yücek and Arslan, A survey of spectrum sensing algorithms for cognitive radio. IEEE Comms. Surveys and Tutorials, 2009.
Survey of wideband spectrum sensing and sub-Nyquist approaches. arXiv:2001.02574.
DECISION POLICY
Sutton and Barto, Reinforcement Learning: An Introduction, 2nd ed. MIT Press, 2018.
Auer, Cesa-Bianchi and Fischer, Finite-time analysis of the multiarmed bandit problem. Machine Learning 47, 2002.
Mnih et al., Human-level control through deep reinforcement learning. Nature 518, 2015.
PERIOD ESTIMATION
Mardia and Jupp, Directional Statistics. Wiley, 2000 — Rayleigh test, mean resultant length.
VanderPlas, Understanding the Lomb-Scargle periodogram. ApJS 236, 2018.
6
Notes: Two things to land here. First, the green column: the sweep still beats us on distinct bursts caught, and we left the row in. Second, the patent. Somebody has tried reinforcement learning on receiver scan scheduling before, we found it, and we can say what is different about ours, which is the periodicity feature feeding the state. If a judge asks whether the numbers are reproducible, the answer is one script from a clean checkout.